Work:	ISA8895 Implementation
Section:	Structure
Chapter:	Physical Asset
Language:	English
Version:	V3 - 05/2011

---
Agenda
Agenda
- Introduction
- ISA88/95 Physical hierarchy model
- ISA88 Equipment entity model
  - Process Cell / Work Center
  - Unit / Work Unit
  - Equipment Module
  - Control Module
  - Device Module
  - Exploit the model
- ISA95 Hierarchy scope
- ISA95 Equipment Model
- Practice

---
CC functional domains
CC functional domains
ISA-95
ISA-88
TOGAF
ITIL
ISA-88 + ISA-95
Product Asset Management
Physical Asset Management
Human Asset Management
IT Asset Management
Inventory Asset Management

---
Information Elements
Information Elements
Domain	Model	Std	Information elements
Product Asset	Product / Product	ISA88 / ISA95	Product Hierarchy / Product Definition
Inventory Asset	Material	ISA95	Material Resources
Physical Asset	Physical / Equipment	ISA88 / ISA95	Equipment Hierarchy / Equipment Resources
Human Asset	Personnel	- / ISA95	Personnel Hierarchy / Personnel Resources
Equipment Control	Procedural	ISA88	Functional Hierarchy / Equipment Procedural Elements
Physical Process Control	Procedural	ISA88	Physical Processes / Procedural Elements / Physical Process Transform Components
Physical Process Mngt	Segment	ISA95	Segments
Operation Process Mngt	Operation Activity	ISA95	Operation Processes / Activities / Tasks

---
Objectives of the physical asset modeling
Objectives of the physical asset modeling
Provide to the system a depiction of the actual composition of the facility
  - We build a consistent image of the world from our social and cultural environment, our senses, our experiences
  - The quite limited perception and computing capabilities of an information system imposes to provide it a structured, preformatted view of its physical environment.
- This view may be
  - Rigid = corresponding to a typical assembly of its constituting equipment
  - Dynamic = linked to the functional objective of the considered instant
    - “meccano” view of an entirely dismantled facility, assembled at need to execute a particular “process oriented” functionality

---
Who’s / What’s concerned?
Who’s / What’s concerned?
PRM	Usr/Rsp	Usage	Typ.IT app
Customer order processing
Production planning & scheduling	X
Production control	X
Material and energy control
Procurement
Quality assurance	X
Product inventory control
Product cost accounting	X
Product shipping administration
Maintenance management	R
Research & development	X
Engineering	X
Marketing and sales
Finances	X
Human Resources
Information technologies

---
Models overview
Models overview
- The Physical asset models identify the enterprise physical aspects
- Enterprise physical nature is described in a hierarchical manner
- 2 models address physical asset modelling
  - ISA88/95 Physical hierarchy model
  - ISA95 Equipment Model
- By physical, ISA- and ISA-95 refer to 2 different concepts
  - Topology as geographical location such as a workshop, a plant (as logical concepts for designating a place or an organizational entity)
  - “Equipment entities” that can be a machine, a facility (as a collection of equipment)
Still quite fuzzy in ISA-95
ISA-88 made some progress by distinguising a physical model for the topology and an Equipment entity model (that associate “control” to make these entity “processing enabled”

---
Agenda
Agenda
- Introduction
- ISA88/95 Physical hierarchy model
- ISA88 Equipment entity model
  - Process Cell / Work Center
  - Unit / Work Unit
  - Equipment Module
  - Control Module
  - Device Module
  - Exploit the model
- ISA95 Hierarchy scope
- ISA95 Equipment Model
- Practice

---
ISA88/95 Physical Hierarchy Model
ISA88/95 Physical Hierarchy Model
This model is global, covering the industrial part of the enterprise
  - Describes the general organization of physical assets hierarchically
  - Matches one aspect of the enterprise decisional structure
  - The ISA88 model was initially ”Batch Oriented”
  - ISA95 extends it to cover the whole production system
  - CCM extends it to cover the financial aspects
- This model is not very constraining,
  - The upper levels describe the logical organization of the enterprise, to match any organisational structures – not to guide organization
  - Lower levels are more prescriptive and must be respected, but they can be (mostly) omitted or extended
- Both ISA88 and ISA95 are critically bound to this model
  - The information system is primarily structured around this model
  - The lower levels starting at the Work Center (Process Cell) level are specifically relevant for the ISA88 standard

---
ISA88 Physical Model
ISA88 Physical Model
ENTERPRISE
7 levels are defined :
  - Organizational Upper levels
    - Entreprise, Site, Area
  - Technical Lower levels
    - Process Cell, Unit, Equipment Module, Control Module
    - Address flexibility
  - Control Modules (Lowest level) correspond to the actual equipment.
    - Other level are compositions of lower levels
SITE
AREA
PROCESS CELL
UNIT
EQUIPMENT
MODULE
CONTROL
MODULE

---
ISA95 extended physical model (Actual Facility layout)
ISA95 extended physical model (Actual Facility layout)
ENTERPRISE
SITE
AREA
WORK
CENTER
WORK UNIT
EQUIPMENT
MODULE
CONTROL
MODULE
PROCESS
CELL
UNIT
BATCH
PROCESS
(ISA88)
PRODUCTION
UNIT
UNIT
CONTINUOUS
PROCESS
PRODUCTION
LINE
WORK CELL
DISCRETE
PROCESS
STORAGE
ZONE
STORAGE
UNIT
WAREHOUSE

---
Upper physical level modeling
Upper physical level modeling
Enterprise, Site, Area, Process cell
  - No technical constraints
  - Based on organizational considerations
  - A Process cell corresponds at least to the scope of the Recipes or Process Orders / Production Requests
ENTERPRISE
SITE
AREA
WORK CENTER
UNIT
EQUIPMENT
MODULE
CONTROL
MODULE

---
Example of upper level modeling
Example of upper level modeling
Enterprise
LFA & Co
Sites
Lyon
Frankfurt
Atlanta
Area
Production
Storage / Shipment
Utilities
Building A
Building B
Finihed
products
Raw
material
Control &
Packaging
Steam
generation
Work Center

---
Example of upper level modeling
Example of upper level modeling
Work Centers
Storage zone
Raw material
Storage zone
Finish products
Process Cell
Preparation
Process Cell
Production 1
Production Line
Packaging
Areas
Process Cell
Production 2
N2
Steam
Water
Power
Gazeous effluents
Condensats
Waste water
Heat
Process Cell
Utilities

---
Extended Physical & Decisional hierarchy
Extended Physical & Decisional hierarchy
Shareholders
Financial
management
Company
Enterprise
Planning
Site
Area
Scheduling
Work Center
Work Unit
Equipment Module
Operations
Control Module

---
Agenda
Agenda
- Introduction
- ISA88/95 Physical hierarchy model
- ISA88 Equipment entity model
  - Process Cell / Work Center
  - Unit / Work Unit
  - Equipment Module
  - Control Module
  - Device Module
  - Exploit the model
- ISA95 Hierarchy scope
- ISA95 Equipment Model
- Practice

---
Combining Production / Industrial Information Systems
Combining Production / Industrial Information Systems
Production System as a physical entity is the Framework (ISA88)
  - Physical hierarchy corresponds to Decision hierarchy
  - Any Information service or process is embedded within a specific Equipment entity, at any level
    - IIS doesn’t exist by itself in the vacuum…
  - Information system is a supporting system, not a leading entity
- Any part of the production system might need IIS support
  - Or can live without it
- Equipment elements are equipment entities when associated with information processing features

---
Equipment Entity embeds Equipment & Information
Equipment Entity embeds Equipment & Information
Equipment
Element
Equipment
Entity
Business Process Management
Physical Process Management
Physical Process Control
Equipment Control
Information
Processing
FT

---
Equipment Entity – Example 1
Equipment Entity – Example 1
Command
Run pump
at rate X
Status
Pump running
At rate X
Physical Equipment
Information Processing
Basic
Procedural
Coordination
S
FT
E
E
E
E
E
E
C
Equipment Entity

---
Equipment Entity – Example 2
Equipment Entity – Example 2
Command
Request Process
capabilities
Status / Response
Processing Capabilities
Catalog
Physical Equipment
Information Processing
Process segment
Definition lookup
E
E
E
E
E
E
C
Equipment Entity

---
Equipment Entity – Example 3
Equipment Entity – Example 3
Command
Optimize Orders’
Scheduling
Status / Response
Optimized
Orders’ schedule
Physical Equipment
Information Processing
Schedule Orders
E
E
E
E
E
E
C
Equipment Entity

---
Information & Equipement
Information & Equipement
The physical model is the primary framework of information system
  - All functional elements, resources, documents rest on this model
  - No information can be defined outside the context of an equipment entity – its physical scope
	Ent.	Site	Area	Pcell	Unit	EM	CM
Basic control							X
Coordination control			X	X	X	X	X
Procedural control (Equipment)				X	X	X
Procedural control (Recipes)				X	X
Product definition	X	X
Objects classes	X

---
ISA88 definition for lower physical hierarchy model
ISA88 definition for lower physical hierarchy model
Process cell
  - A logical grouping of equipment required for production of one or more batches
- Units
  - A collection of related control modules and equipment modules that can carry out one or more processing activities
- Equipment modules
  - A functional group of equipment and/or control modules that can carry out a finite number of specific processing activities
- Control modules
  - A regulating device, a state oriented device, or a combination of both that is operated as a single device

---
Agenda
Agenda
- Introduction
- ISA88/95 Physical hierarchy model
- ISA88 Equipment entity model
  - Process Cell / Work Center
  - Unit / Work Unit
  - Equipment Module
  - Control Module
  - Device Module
  - Exploit the model
- ISA95 Hierarchy scope
- ISA95 Equipment Model
- Practice

---
Role of the Work Center
Role of the Work Center
A work centre needs to encompass all the needed Work Units to make a defined product
  - The scope of a Production Request
- Essentially an organizational level
  - Activity, topology
  - No hard constraints
  - Might help for facilities classification
    - Ability to replicate a Work Center template
PROCESS CELL
UNIT
EQUIPMENT
MODULE
CONTROL
MODULE

---
Work Center for Batch: Process Cell
Work Center for Batch: Process Cell
Definition
  - A logical grouping of equipment (Units) required for the production of one or more batches
- Properties
  - May contain more than one grouping of equipment needed to make a batch
    - “Train”
  - The equipment actually used for the batch is referred to as the path
  - May contain more than one batch at a time (possibly several independent production order being processed simultaneously)
PROCESS CELL
UNIT
EQUIPMENT
MODULE
CONTROL
MODULE

---
Work Center for Batch: Process Cell
Work Center for Batch: Process Cell
Rules
  - Static geographical structure, defined at the engineering time
  - The batch maintains its integrity
  - The scope of a recipe or production request
  - The action scope of an operator
  - Bounded by input / output material storage (raw matierial / semi-finished products / finished products
- Examples
  - Building B6
  - Finishing workshop
PROCESS CELL
UNIT
EQUIPMENT
MODULE
CONTROL
MODULE

---
Process Cell Structures
Process Cell Structures
Single-Path
“Raw”
Material
Storage
Multiple-Path
“Raw”
Material
Storage
“Finished”
Material
Storage
Unit 2
Unit 1
“Finished”
Material
Storage
Unit 2
Unit 1
PROCESS CELL
UNIT
EQUIPMENT
MODULE
CONTROL
MODULE

---
Networked-Path Process Cell Structure
Networked-Path Process Cell Structure
“Raw”
Material
Storage
“Finished”
Material
Storage
Unit 2
Unit 1
Unit 4
Unit 3
PROCESS CELL
UNIT
EQUIPMENT
MODULE
CONTROL
MODULE

---
Example of a 2-Unit Process Cell
Example of a 2-Unit Process Cell
Reactor
M
F1
PIC
PIC
Premixer
M
Ingredient A
Ingredient B
PROCESS CELL
UNIT
EQUIPMENT
MODULE
CONTROL
MODULE

---
Example of a 4-Unit Process Cell
Example of a 4-Unit Process Cell
PIC
N2
Vent
Premix1
PIC
N2
VENT
Premix2
PIC
N2
Vent
Rxtr 1
TIC
Steam
C-H2O
Cond
H2O-R
PIC
N2
Vent
Rxtr 2
TIC
Steam
C-H2O
Cond
H2O-R
Catalyst
Catalyst
FQIC
#1
FQIC
#2
FQIC
#3
FQIC
#4
LI
WI
LI
FSL
FSL
V1
V3
V11
V12
V11
V12
V11
V12
V11
V12
V1
V1
V1
V2
V4
V5
V5
V1
V6
V7
V8
V6
V7
V8
V10
V10
V13
V14
V15
V16
V13
V14
V15
V16
PROCESS CELL
UNIT
EQUIPMENT
MODULE
CONTROL
MODULE

---
Agenda
Agenda
- Introduction
- ISA88/95 Physical hierarchy model
- ISA88 Equipment entity model
  - Process Cell / Work Center
  - Unit / Work Unit
  - Equipment Module
  - Control Module
  - Device Module
  - Exploit the model
- ISA95 Hierarchy scope
- ISA95 Equipment Model
- Practice

---
Role of Work Unit
Role of Work Unit
The « Central » allocation level
  - A relatively autonomous entity for planning/scheduling purpose
  - Batch Processes,
    - A strict batch breakdown : Unit contains one single batch
  - Discrete Processes,
    - Work Cell is similar to Unit
  - Warehouses and storage :
    - Allocation is not confined to a specific level
    - Storage Units should be recursive – not in the standard
  - Continuous processes
    - A main equipment, Sub-part of a Production Unit
    - Can segregate “virtual batches” in a continuous flow
- Provides and execute product independent process services
  - Implemented by Equipment Procedural Element (EPE) (possibly inherited from embedded Equipment Modules)
PROCESS CELL
UNIT
EQUIPMENT
MODULE
CONTROL
MODULE

---
Work Units for Batch: Unit
Work Units for Batch: Unit
Definition
  - Is a collection of Control Modules and Equiment Modules
  - Performs one or more significant processing activities, as product independent Equipment procedural Elements
      - Combining material, Performing a reaction
- Role
  - Basis of procedural control
- Properties
  - Cannot contain another unit
  - A unit cannot operate on more than one batch of material at any given time
    - Although a unit is allowed to operate on a portion of a single batch
  - Making a batch often requires multiple units
    - Although a batch is allowed to be completed in a single unit
  - May contain a flexible amount of control modules and/or equipment modules
    - Permanently attached parts to a unit
    - Temporarily attached parts to a unit
    - Totally separate from any unit
PROCESS CELL
UNIT
EQUIPMENT
MODULE
CONTROL
MODULE

---
Work Units for Batch: Unit
Work Units for Batch: Unit
Rules
  - Essentially dynamic structure, : identified at the engineering time, but physical scope depends on the context
  - Centered around a major piece of equipment
  - Autonomy: May operate independently of other units
- Examples
  - Reactor, Mixer
  - Washing machine
  - Oven
  - Press
PROCESS CELL
UNIT
EQUIPMENT
MODULE
CONTROL
MODULE

---
Example of a Unit in a Process Cell
Example of a Unit in a Process Cell
PIC
N2
Vent
Premix1
PIC
N2
VENT
Premix2
PIC
N2
Vent
Rxtr 1
TIC
Steam
C-H2O
Cond
H2O-R
PIC
N2
Vent
Rxtr 2
TIC
Steam
C-H2O
Cond
H2O-R
Catalyst
Catalyst
FQIC
#1
FQIC
#2
FQIC
#3
FQIC
#4
LI
WI
LI
FSL
FSL
V1
V3
V11
V12
V11
V12
V11
V12
V11
V12
V1
V1
V1
V2
V4
V5
V5
V1
V6
V7
V8
V6
V7
V8
V10
V10
V13
V14
V15
V16
V13
V14
V15
V16
PROCESS CELL
UNIT
EQUIPMENT
MODULE
CONTROL
MODULE

---
Agenda
Agenda
- Introduction
- ISA88/95 Physical hierarchy model
- ISA88 Equipment entity model
  - Process Cell / Work Center
  - Unit / Work Unit
  - Equipment Module
  - Control Module
  - Device Module
  - Exploit the model
- ISA95 Hierarchy scope
- ISA95 Equipment Model
- Practice

---
Roles of Equipment modules
Roles of Equipment modules
2 roles
  - Breakdown of a Work unit
    - May be used to limit the scope of an EPE
    - Units building blocks
  - Shared equipment having autonomous process capabilities that can be used with several units
    - Non-exclusive: distribution of utilities (air, steam, N2, water)
    - Exclusive: Charging device, transfer lines
- Not a mandatory element
PROCESS CELL
UNIT
EQUIPMENT
MODULE
CONTROL
MODULE

---
Equipment Modules
Equipment Modules
Definition
  - A collection of equipment and/or control modules that can carry out a finite number of specific processing activities
    - Implements Equipment Procedural Elements by commanding control modules or lower level equipment modules
      - An Equipment module without EPEs is a Control Module
      - An equipment module is technically similar to a unit
- Properties
  - May contain other EMs
  - Dependent: May be part of a single Work Unit or another Equipment Module for its exclusive usage
  - Autonomous: May be part of a Work Center
    - can be temporarily “attached” to a Work Unit as a common resource
    - Can be used in conjunction with several Work Units or other Equipment Modules, or even running independently
PROCESS CELL
UNIT
EQUIPMENT
MODULE
CONTROL
MODULE

---
Equipment Modules
Equipment Modules
Rules
  - Essentially dynamic structure, : identified at the engineering time, but physical scope depends on the context
  - Inherited from the Work Unit (part of it)
  - Usually centered around a piece of process equipment such as a process heater or weight tank
- Examples
  - Weight tank used by a single unit
  - A filter that is only used by a single unit
  - Weight tank shared by multiple units, but only usable by a single unit at a time
    (an exclusive use resource)
  - An ingredient supply system that shared by multiple units and can be used by many simultaneously (a shared-use resource)
PROCESS CELL
UNIT
EQUIPMENT
MODULE
CONTROL
MODULE

---
Equipment Module Implementations
Equipment Module Implementations
Option 1: No equipment modules
  - Any EPE of a Unit can allocate (dynamically) any control module within the Work Center / Process Cell
  - A single EPE can execute a transfer between 2 units
- Option 2: Units without EPEs inheriting EPEs from EMs
  - Typically for embedded equipment modules
- Option 3: Units with EPEs commanding EPEs from EMs
  - Typically for shared equipment modules
PROCESS CELL
UNIT
EQUIPMENT
MODULE
CONTROL
MODULE

---
Example of an EM in a Process Cell
Example of an EM in a Process Cell
PIC
N2
Vent
Premix1
PIC
N2
VENT
Premix2
PIC
N2
Vent
Rxtr 1
TIC
Steam
C-H2O
Cond
H2O-R
PIC
N2
Vent
Rxtr 2
TIC
Steam
C-H2O
Cond
H2O-R
Catalyst
Catalyst
FQIC
#1
FQIC
#2
FQIC
#3
FQIC
#4
LI
WI
LI
FSL
FSL
V1
V3
V11
V12
V11
V12
V11
V12
V11
V12
V1
V1
V1
V2
V4
V5
V5
V1
V6
V7
V8
V6
V7
V8
V10
V10
V13
V14
V15
V16
V13
V14
V15
V16
PROCESS CELL
UNIT
EQUIPMENT
MODULE
CONTROL
MODULE

---
Agenda
Agenda
- Introduction
- ISA88/95 Physical hierarchy model
- ISA88 Equipment entity model
  - Process Cell / Work Center
  - Unit / Work Unit
  - Equipment Module
  - Control Module
  - Device Module
  - Exploit the model
- ISA95 Hierarchy scope
- ISA95 Equipment Model
- Practice

---
Role of Control modules
Role of Control modules
The lowest, mandatory level in the Physical Hierarchy
  - The only actual equipment entity: all upper level are organizational views with larger or smaller focus
  - The only acting entity (move actuators, run motors)
- Mechanical engineering consistency
  - CM breakdown corresponds to generic equipment entities
- Simplification of control:
  - Execute elementary equipment services invoked by EPEs
- Functional leveling of technological variants
  - Same interface and capabilities, specific control
- Prevent conflicting equipment usage
  - EPEs can explicitly allocate control modules providing an inherent interlock between conflicting functionalities
PROCESS CELL
UNIT
EQUIPMENT
MODULE
CONTROL
MODULE

---
Control Modules
Control Modules
Definition
  - A piece of processing equipment with associated collection of sensors, actuators, and other control modules
- Properties
  - Every piece of equipment is controlled by one (and only one) control module
  - The lowest, mandatory physical level
    - Any part of the actual equipmeNT is part of one, and only one control module
  - Provides the only connection to the process
    - Control modules can content instrumentation
    - But Control Modules ARE NOT instruments (see Device Modules)
  - Acts as a single entity from a control standpoint
  - Do not contain / cannot execute procedural elements
  - The only real physical entity
    - All upper levels are more or less focused orgainsational views
  - Unknown by the Recipe
PROCESS CELL
UNIT
EQUIPMENT
MODULE
CONTROL
MODULE

---
Control modules and flow analysis
Control modules and flow analysis
Rules
  - None in ISA88
- WBF Flow analysis concepts:
  - Physical flows get through tangible equipment entities (Control modules)
  - A proper breakdown allows to control flows regardless the functional intent. Control modules control … flows
  - Breakdown rules for control modules
    - CMs are elementary flow sections
    - Extension of Delta Nodes / Astrid methodologies
  - The resulting breakdown highlights consistent generic equipment entities
PROCESS CELL
UNIT
EQUIPMENT
MODULE
CONTROL
MODULE

---
Flow Analysis rules for breaking down a facility into CMs
Flow Analysis rules for breaking down a facility into CMs
Identify all flow breaking devices
  - Shut-off valves
  - Doors
  - Traffic lights
  - Removable pipe / Blind flanges
  - …
- Control modules are bounded by these devices
- Several flows may run through a given equipment
  - This equipment may be split into several control modules
    - Liquid and gaseous part of a tank
PROCESS CELL
UNIT
EQUIPMENT
MODULE
CONTROL
MODULE

---
Control Module examples
Control Module examples
Commands
States
Circulate
Circulating
Sending
To Process
Stop
Stopped
	Circulate	ToProcess	Stop
Start Pompe	1	1	0
Stop Pompe	0	0	1
Open Recirc XV	1	0	1
Close Recirc XV	0	1	0
Open Process XV	0	1	0
Close Process XV	1	0	1
Process XV
Recirc XV
Pump
PROCESS CELL
UNIT
EQUIPMENT
MODULE
CONTROL
MODULE

---
Control Module examples
Control Module examples
CM4
CM2
PID
PID
CM3
CM1
PID
HIC
HIC
PROCESS CELL
UNIT
EQUIPMENT
MODULE
CONTROL
MODULE

---
Control Module examples
Control Module examples
Raw_Matl_Req as enum:
0 None
1 Cream
2 Milk
3 Corn Syrup
4 Water
Material Selection Control Module
Define Discharge_Flow_SP as
0 - 60 GPM
Define Recirc_Flow_SP as
0 - 60 GPM
Define CIP_Flow_SP as
0 - 140 GPM
S
FT
Pump
Control Module
PROCESS CELL
UNIT
EQUIPMENT
MODULE
CONTROL
MODULE

---
Agenda
Agenda
- Introduction
- ISA88/95 Physical hierarchy model
- ISA88 Equipment entity model
  - Process Cell / Work Center
  - Unit / Work Unit
  - Equipment Module
  - Control Module
  - Device Module
  - Exploit the model
- ISA95 Hierarchy scope
- ISA95 Equipment Model
- Practice

---
Device Module
Device Module
- Sensors and actuators are not defined in the standard
- Sensors and actuators can be considered as:
  - First level control modules
    - Possible because of the recursive nature of the control module
    - Common practice
  - Device modules, an additional element
    - The standard allows extensions
    - Allows to preserve the true nature of the Control Module as an abstraction layer: a control module does not necessarily hold instruments…
    - Proposed in ISA88 part 5
PROCESS CELL
UNIT
EQUIPMENT
MODULE
CONTROL
MODULE
DEVICE
MODULE

---
Flow Analysis: Device modules attachment to CMs
Flow Analysis: Device modules attachment to CMs
- DM are attached to the supporting CM
- Flow breaking devices are between 2 or more CMs. They may be considered as:
  - Independent CMs : More flexible, WBF current work proposed approach (Directing nodes)
  - Device modules attached to one of the adjacent CM (Current ASTRID or DELTA NODE methods)
    - Rule 1: A flow breaking device is attached to the upstream CM
    - Rule 2: A flow breaking device is attached to the user of a shared flow (utility for example)
    - Rule 3: The second rule prevails on the first one
PROCESS CELL
UNIT
EQUIPMENT
MODULE
CONTROL
MODULE
DEVICE
MODULE

---
Device safety and control
Device safety and control
Operator (HMI)
Adjacent CM
(Flow control)
Owning CM
(automatic control)
Automatic control
Manual
control
Interlocking task
Product and equipment protection
Flow interlocks
Flow integrity
Acting device
Content compatibility
Safety task
Personnel and environment protection
(external safety system)
Capacity constraints
Commands
Flow Information
Interlock
PROCESS CELL
UNIT
EQUIPMENT
MODULE
CONTROL
MODULE
DEVICE
MODULE

---
A Motor Device Module
A Motor Device Module
Single-Speed Motor
Module
Starter
Coil
Rotation
Sensor
Motor
Start
Stop
Run
Fail
Commands
Status
PROCESS CELL
UNIT
EQUIPMENT
MODULE
CONTROL
MODULE
DEVICE
MODULE

---
Agenda
Agenda
- Introduction
- ISA88/95 Physical hierarchy model
- ISA88 Equipment entity model
  - Process Cell / Work Center
  - Unit / Work Unit
  - Equipment Module
  - Control Module
  - Device Module
  - Exploit the model
- ISA95 Hierarchy scope
- ISA95 Equipment Model
- Practice

---
Equipment Modules vs. Control Modules
Equipment Modules vs. Control Modules
Equipment Module	Control Module
Can contain an EPE	Cannot contain an EPE
Must interface to the process via a control module	Directly interfaces to the process via Device Modules
Commonly used as stand alone and shared equipment by other Units or EMs
Commonly used to deal with transfers
Can contain other EMs and CMs	Can contain other CMS, not EMs
May have a direct link to the recipe procedure via the EPE	Has no direct link to the recipe procedure

---
Control modules and Equipment modules : Unit ownership
Control modules and Equipment modules : Unit ownership
By design, CMs and EMs
  - can be attached permanently to a unit
  - Can be independent of any unit, part of the whole Process Cell / Work Center
    - CM et EM can be temporarily attached to any unit to provide the needed Equipment (CMs) or Process (Ems) services needed to achieve its processing function
    - CM and EM can also be commanded independently

---
Example of ISA88 physical hierarchy
Example of ISA88 physical hierarchy
Process Cell
Unit
Unit
EM
EM
EM
CM
EM
CM
CM
CM
CM
CM
CM
CM

---
Example of ISA88 physical hierarchy (Cont’d)
Example of ISA88 physical hierarchy (Cont’d)
Process Cell
Unit1
EM3
Unit2
EM1
EM2
CM1
CM2
CM3
CM4
CM5
CM6
CM7
CM8
CM9
CM10

---
Example of ISA88 physical hierarchy (Cont’d)
Example of ISA88 physical hierarchy (Cont’d)
Process Cell
Unit1
EM3
Unit2
CM1
CM2
CM3
CM4
CM5
CM6
CM7
CM8
CM9
CM10

---
Example of ISA88 physical hierarchy (Cont’d)
Example of ISA88 physical hierarchy (Cont’d)
Process Cell
Unit1
EM3
Unit2
EPE 2
EPE 1
(EM1)
(EM2)
EM3’
EPE 4
CM1
CM2
CM3
CM4
EPE 3
DM1
DM2
DM3
DM4
DM5
DM6
DM7
DM8
DM9
DM10

---
Example of ISA88 physical hierarchy (Cont’d)
Example of ISA88 physical hierarchy (Cont’d)
Process Cell
Unit1
EM3
Unit2
Phase X
Phase Y
EM1
EM2
EM3’
No EM: EPEs
Dynamically allocates
The needed CMs
CM1
CM2
CM3
CM4
DM1
DM2
DM3
DM4
DM5
DM6
DM7
DM8
DM9
DM10

---
Agenda
Agenda
- Introduction
- ISA88/95 Physical hierarchy model
- ISA88 Equipment entity model
  - Process Cell / Work Center
  - Unit / Work Unit
  - Equipment Module
  - Control Module
  - Device Module
  - Exploit the model
- ISA95 Hierarchy scope
- ISA95 Equipment Model
- Practice

---
ISA-95 Hierarchy scope
ISA-95 Hierarchy scope
ISA-95 attaches “Hierarchy scope” to all information objects
  - Resources, process segment, product definition,
  - Previously named “Location”
  - “Hierarchy scope is an attribute used in many other objects. The hierarchy scope attribute identifies where the exchanged information fits within the role based equipment hierarchy. It defines the scope of the exchanged information, such as which site or which area the information is relevant for. The hierarchy scope identifies the associated instance in the role based
- While ISA-88 attaches “control” to the physical hierarchy, ISA-95 takes the other way around: it attaches a physical hierarchy information to information objects

---
Example
Example
ISA-95
ISA-88
Unit
(Equipment Entity)
Process
Segment
(Information object)
Work
Center
(Hierarchy scope)
Procedural
Element
(Control)

---
Agenda
Agenda
- Introduction
- ISA88/95 Physical hierarchy model
- ISA88 Equipment entity model
  - Process Cell / Work Center
  - Unit / Work Unit
  - Equipment Module
  - Control Module
  - Device Module
  - Exploit the model
- ISA95 Hierarchy scope
- ISA95 Equipment Model
- Practice

---
ISA95 equipment models
ISA95 equipment models
These models identify the physical assets
  - by their role in the facility
    - The function performed by a machine at the explicit location
    - Not necessarily always the same, can be replaced without affecting the role
  - By their asset / inventory aspect
    - The unique machine identifiable by its serial number
    - Only for “maintainable” equipments,
      - not all physical – organisational – entities
    - Similar to Inventory asset
- Features
  - Implements the physical hierarchy model
  - Defines properties of physical elements
  - Allows Class based definition

---
ISA95 Equipment Resource Model: Role based Equipment
ISA95 Equipment Resource Model: Role based Equipment

---
ISA95 Equipment Resource Model: Physical Asset
ISA95 Equipment Resource Model: Physical Asset

---
ISA95 global Equipment Resource Model
ISA95 global Equipment Resource Model

---
Agenda
Agenda
- Introduction
- ISA88/95 Physical hierarchy model
- ISA88 Equipment entity model
  - Process Cell / Work Center
  - Unit / Work Unit
  - Equipment Module
  - Control Module
  - Device Module
  - Exploit the model
- ISA95 Hierarchy scope
- ISA95 Equipment Model
- Practice

---
Physical Asset Models elements (common RBE/PhA)
Physical Asset Models elements (common RBE/PhA)
Properties (Definition)
  - “object denoting an implementation specific characteristic of an entity”
  - Characterization entities for Equipment Classes/Equipment
    - Ex: Capacity, Max Pressure, NominalSpeed, NbOfBagsPerMintute …
  - Some properties can match the Equipment constraints defined in Process Element (Product Asset, Process Definition)
- Property (Value)
  - Valuation of the property as a requirement (for Equipment Class/Equipment)
  - Valuation of a property from actual assessment (For Physical Asset)
    - Ex: NbOfBagsPerMintute = 1643
- Test specification
  - “identify a test for one or more equipment properties”
- Test Result
  - “Results from a equipment capability test for a specific piece of equipment / physical asset”

---
Physical Asset Models elements (specific RBE/PhA)
Physical Asset Models elements (specific RBE/PhA)
Role based Equipment
  - Equipment
    - “A representation of the elements of the equipment hierarchy model”
  - Equipment Class
    - “a grouping of role based equipment with similar characteristics for purposes of scheduling and planning”
- Physical Asset
  - Physical Asset
    - represents information about a physical piece of equipment
  - Physical Asset Class
    - “grouping of physical assets with similar characteristics for purposes of repair and replacement”

---
Agenda
Agenda
- Introduction
- ISA88/95 Physical hierarchy model
- ISA88 Equipment entity model
  - Process Cell / Work Center
  - Unit / Work Unit
  - Equipment Module
  - Control Module
  - Device Module
  - Exploit the model
- ISA95 Hierarchy scope
- ISA95 Equipment Model
- Practice

---
Exercise (1) : Unit, Equipment module or Control module?
Exercise (1) : Unit, Equipment module or Control module?
	Is a Unit	Isn’t a Unit (EM or CM)
Reactor
Fluid Bed Dryer
Pasteurizer
Pump
Multi pump set
Ingredient storage tank
Washing machine
Kitchen blender (& cook)
Refrigerator
Dishwasher
Iron
Bred cooker
Oven
Agitator

---
Exercise (2) - Excel spreadsheet
Exercise (2) - Excel spreadsheet
(2.1) Physical Hierarchy
  - Give possible names and examples for the physical hierarchy level

---
PIC
N2
Vent
Premix1
PIC
N2
VENT
Premix2
PIC
N2
Vent
Rxtr 1
TIC
Steam
C-H2O
Cond
H2O-R
PIC
N2
Vent
Rxtr 2
TIC
Steam
C-H2O
Cond
H2O-R
Catalyst
Catalyst
FQIC
#1
FQIC
#2
FQIC
#3
FQIC
#4
LI
WI
LI
FSL
FSL
V1
V3
V11
V12
V11
V12
V11
V12
V11
V12
V1
V1
V1
V2
V4
V5
V5
V1
V6
V7
V8
V6
V7
V8
V10
V10
V13
V14
V15
V16
V13
V14
V15
V16

---
Exercise (3) : Excel spreadsheet - Physical modeling
Exercise (3) : Excel spreadsheet - Physical modeling
(1.1) Properties
  - Identify some typical equipment properties: name, range,
- (1.2) Equipment Test Specification
  - Identify typical Test Specifications
- (2.2) Equipment classes
  - Identify certain Equipment roles, For different level: WU, EM, CM, DM
- (2.3) Equipment
  - identify
    - Enterprise, Site, Area, Work Centers/Process Cells
    - Work Units / Units, Device Modules, Flow breaking devices
    - Control modules: Within the process cell, Peripheral facilities: storage, utilities
- (3.1) Physical Asset Hierarchy
  - Identify a possible maintenance oriented physical hierarchy
- (3.2) Physical Asset Class
  - Identify certain machines types
- (3.3) Physical Asset
  - Identify certain machines

---
Thank You !